## Slide 1: CAN Gateway and Translation Specifications
07.12.2022

## Slide 2: Communication Block Diagram
Arduino
CAN0
CAN1
CAN Bridge Translator
CAN BUS 0
CAN BUS 1
VEHICLE
CAN 0
CAN 1

## Slide 3: CAR Configuration
Update config.h to configure the target vehicle; ENV200 or LEAF
// Vehicle selection
// Requirement: Uncomment the target vehicle; Comment the unused vehicle
//#define CAN_BRIDGE_FOR_ENV200
#define CAN_BRIDGE_FOR_LEAF

## Slide 4: CAN Rx Mode Selection
Update config.h to configure the CAN Rx Mode; Interrupt or Polling
// CAN Rx MODE Selection
// When mode is polling, checking of CAN reception is every Xms (refer timer interrupt period configuration)
// When mode is interrupt, checking of CAN reception is every falling edge of MCP2515 INT pin
// Requirement: Uncomment only 1 mode
#define CAN_MODE_INTERRUPT
//#define CAN_MODE_POLLING

## Slide 5: [ENV200] Requirement #01: ID 0x1F2
IF CAN ID 0x1F2 is received THEN
  Copy frame.data[2] to charging_state
  To be confirmed: What to do with charging_state?
  Temp behavior: Display entire CAN frame in debug window
END IF

## Slide 6: [ENV200] Requirement #02: ID 0x55B
IF CAN ID 0x55B is received THEN
  instrumentCluster5E3 = {.can_id = 0x5E3, .can_dlc = 5, .data = {0x8E,0x00,0x00,0x00,0x80}}
IF ID is received from CAN BUS 0 THEN
Send instrumentCluster5E3 to CAN BUS 1
ELSE //received from CAN BUS 1
Send instrumentCluster5E3 to CAN BUS 0
END IF
END IF

## Slide 7: [ENV200] Requirement #03: ID 0x5BC
IF CAN ID 0x5BC is received THEN
IF ID is received from CAN BUS 0 THEN
Send translated value to CAN BUS 1
ELSE //received from CAN BUS 1
Send translated value to CAN BUS 0
END IF
END IF

## Slide 8: [ENV200] Requirement #04: ID 0x59E
IF CAN ID 0x59E is received THEN
IF ID is received from CAN BUS 0 THEN
Send translated value to CAN BUS 1 with CRC
ELSE //received from CAN BUS 1
Send translated value to CAN BUS 0 with CRC
END IF
END IF

## Slide 9: [LEAF] Requirement #05: ID 0x1DC
IF CAN ID 0x1DC is received THEN
IF ID is received from CAN BUS 0 THEN
Send translated value to CAN BUS 1 with CRC
ELSE //received from CAN BUS 1
Send translated value to CAN BUS 0 with CRC
END IF
END IF